## Slide 1: Firmware Updates for Internet of Things Devices (SUIT)

## Slide 2: SUIT Software Updates for Internet of Things
Source Code v1 -> Binary Firmware
Source Code v2 -> New Binary Firmware
In trusted environment (e.g., production)
✔
+Manifest to validate
firmware is not bogus
Certificates / Keys / etc.
New Firmware
✔

## Slide 3: Our Goal
Input to the recently formed SUIT WG
Creating signed manifest
  Encoded in CBOR
  COSE signed with ECDSA.
Manifest & firmware transport to IoT board via UART.
Bootloader verifies received manifest and installs new firmware.
Firmware + Manifest
Via UART
K64F

## Slide 4: Who participated?
Markus Gueller (Infineon) *
Max Groening (Texas Instruments) *
Hannes Tschofenig (Arm)
Brendan Moran (Arm) – remote *
Jaime Jiménez (Ericsson)
Alexander Pelov (Acklio)
*: New participants

## Slide 5: What was accomplished?
Got development environments working (online IDE, desktop IDE, CLI) on different OSs.
Running code:
  Code for manifest generation (in Python) working.
  Pseudo-bootloader running on IoT board
  UART communication to load firmware working
Keys and example manifests created.
Code for manifest verification (C) in progress.
Walkthrough on Etherpad: http://etherpad.tools.ietf.org:9000/p/FUIETF101

## Slide 6: Lessons Learned
Low level IoT development is hard:
  Setup of development environment & Python took some time.
  UART communication setup
  Debugging is more complex
COSE C library was difficult to use for embedded environment.
  We needed a C implementation that uses the embedded crypto (instead of OpenSSL).
Basic manifest functionality worked fine.